## Slide 2: Outline
Monthly Mean Climatologies
Information of the procedure, data available, and other things
Sample snapshots of grids made with Basemap and matplotlib
More sample vertical cross sections
Discrepancies existing in the climatologies
Tropospheric and Stratospheric Ozone Climatologies
Background Information
Samples of Tropospheric and Stratospheric Ozone
Preliminary Results
Analysis of surface ozone and cross sectioned stratospheric intrusion
Analysis of Western lateral boundary conditions

## Slide 3: Monthly Mean Climatologies

## Slide 4: Information
Global
Information obtained from ECMWF
Resolution of 1.125° x 1.125° (320 longitudinal grid points, 161 latitudinal grid points)
Spanning 59 constant pressure levels, from 1000 hPa to 0.1 hPa
Based on MACC Reanalysis dataset
Available in FST format

## Slide 5: Available Species
Species and parameters available are:
  GEMS Ozone
  Carbon Monoxide
  Methane
  Three dust aerosol bins
    0.03 - 0.55 μm
    0.55 - 0.90 μm
    0.90 - 20.0 μm
  Formaldehyde
  Nitrogen Oxides
  Sulphate Aerosol bin
  Sulphur Dioxide
  Specific Humidity*
Units are uniformly kg * kg-1
*not plotted

## Slide 6: ECMWF - NCDF Specifications
Each NCDF file is sourced from the ECMWF public datasets found at the ECMWF Parameter database.
The files are defined over 60 levels,
The ones used to create the FST files can be found at
  /space/hall1/sitestore/eccc/aq/r1/alh002/NCDF/SPECIES/
They’re separated by parameter name (as defined by ECMWF) and each file is separated by year, and each dataset is defined globally
There also exist natural log surface pressure data at /space/hall1/sitestore/eccc/aq/r1/alh002/NCDF/LNSP/

## Slide 7: Here are some figures over April

## Slide 28: Here are a couple vertical cross sections taken from zonal means

## Slide 29: Sample – Vertical Cross Section for September – GEMS Ozone

## Slide 30: Samples – CO Animated Vertical Cross Section

## Slide 31: Directories
You can find the lat-lon grids for each month (starting from 0 as January, up to 11 as December) at
  /home/ords/aq/alh002/latlon
  Seperated by month directories -> species name
  DST1 is smallest dust bin (0.03 - 0.55 μm), DST3 is biggest dust bin (0.90 - 20.0 μm), SAMR is Sulphate Aerosol Mixing Ratio (Sulphate Aerosol bin)
You can find the vertical cross sections for each month and species at
  /home/ords/aq/alh002/vcross
  Separated by file

## Slide 32: Discrepancies
Very high altitudes often provide strange patterns or no data at all
  Nonexistent data is generally predictably found in larger aerosols
“Proceed with caution” when analyzing high altitude lat-lon grids

## Slide 33: Sample – February GO3 @ 0.1 hPa

## Slide 34: Sample – August GO3 @ 0.1 hPa

## Slide 35: Sample – October GO3 @ 0.1 hPa

## Slide 36: Sample – August HCHO @ 0.1 hPa

## Slide 37: Discrepancies
Sulphur dioxide was only analyzed for the years of 2009 to 2012
  Data exists from October 24th, 2008 to the end of 2008 but was not included, however it can be retrieved from NCDF directory
  Directory: /space/hall1/sitestore/eccc/aq/r1/alh002/NCDF/SPECIES/SO2/INCOMPLETE

## Slide 38: Tropospheric and stratospheric climatologies

## Slide 39: Background Information
Previously, using chemical lateral boundary conditions (CLBC) from MACC Reanalysis (updated every 6 hours) has been shown to improve surface ozone prediction during stratospheric intrusion events
The DynOzone method uses ozonesonde data to provide CLBC’s for the regional GEM-MACH model
Using the CLBC’s defined by the ozonesonde dataset worked the better define the ozone field in the tropopause region, but tropospheric ozone was generally too high. This resulted in better definition of the surface ozone but overexpression of tropospheric ozone nonetheless
The following second half of the presentation will display some results using the DynOzone + MACC Reanalysis derived CLBC’s, along with comparisons to DynOzone + Ozonesonde, MOZART4 (seasonal averaged), and MACC Reanalysis derived CLBC’s

## Slide 40
Averaged (2008 -2012) Tropospheric Ozone @ 100mb through January

## Slide 41
Averaged (2008 -2012) Stratospheric Ozone @ 100mb through January

## Slide 42
Averaged (2008 -2012) Tropospheric Ozone @ 500mb through January

## Slide 43
Averaged (2008 -2012) Stratospheric Ozone @ 500mb through January

## Slide 44
Averaged (2008 -2012) Tropospheric Ozone @ 100mb through July

## Slide 45
Averaged (2008 -2012) Stratospheric Ozone @ 100mb through July

## Slide 46
Averaged (2008 -2012) Tropospheric Ozone @ 500mb through July

## Slide 47
Averaged (2008 -2012) Stratospheric Ozone @ 500mb through July

## Slide 48: Vertical Cross Section of January for Tropospheric Ozone
These figures were made in SPI
The top figure is the vertical cross section
The bottom figure is the area of the cross section
The units, although not specified properly, are kg/kg (as per the ECMWF parameters database)
The reasoning behind the vertical cross section appearing “glitched” is by design - due to filling zeros with nearest non zero value (nearest in tropospheric being the highest level nonzero value)

## Slide 49: Vertical Cross January for Stratospheric Ozone of January
These figures were made in SPI
The top figure is the vertical cross section
The bottom figure is the area of the cross section
The units, although not specified properly, are kg/kg (as per the ECMWF parameters database)
The reasoning behind the vertical cross section appearing “glitched” is by design - due to filling zeros with nearest non zero value (nearest in stratospheric being the lowest level nonzero value)

## Slide 50: Vertical Cross Section of Tropospheric Ozone for July
These figures were made in SPI
The top figure is the vertical cross section
The bottom figure is the area of the cross section
The units, although not specified properly, are kg/kg (as per the ECMWF parameters database)
The reasoning behind the vertical cross section appearing “glitched” is by design - due to filling zeros with nearest non zero value (nearest in tropospheric being the highest level nonzero value)

## Slide 51: Vertical Cross for Stratospheric Ozone of July
These figures were made in SPI
The top figure is the vertical cross section
The bottom figure is the area of the cross section
The units, although not specified properly, are kg/kg (as per the ECMWF parameters database)
The reasoning behind the vertical cross section appearing “glitched” is by design - due to filling zeros with nearest non zero value (nearest in stratospheric being the lowest level nonzero value)

## Slide 52: Preliminary Results
Preliminary results were run on Hadar
The intention of reducing tropospheric ozone in the DynOzone method + MACC Reanalysis dataset looks partially successful
However, the impact of stratospheric intrusion isn’t as prevalent in surface and lower stratospheric ozone levels

## Slide 53: Comparison of the four CLBC strategies modelling the surface level ozone for the regional GEM-MACH at April 13, 2010 21:00:00 GMT. An intrusion can be noted over western United States. The white intersecting contour is the location of the vertical cross sections produced.

## Slide 54: Comparison of the four CLBC strategies modelling the vertical cross section intersecting the stratospheric intrusion in the western United States at April 13, 2010 21:00:00 GMT. An intrusion can be noted over around -117 to -113 degrees on the longitude axis by the sudden increase in tropospheric ozone. The black contour line is a 2.0 PVU contour, and the grey lines are potential temperature

## Slide 55: Stratospheric intrusion analysis/MOZART4
On the surface level, MOZART4 CLBC’s did fairly well in comparison to the three other methods regarding representation of the stratospheric intrusion
It portrays more surface level ozone than the DynOzone + MACC Reanalysis method, and less than both the MACC Reanalysis and DynOzone + Ozonesonde methods

## Slide 56: Stratospheric intrusion/MACC Reanalysis
On the surface level, MACC Reanalysis CLBC’s overly expressed the surface ozone concentrations. This is especially present in the stratospheric intrusion over western United States
It portrays more surface level ozone than the MOZART4 and DynOzone + MACC Reanalysis methods, and less than the DynOzone + Ozonesonde method
Note the high ozone concentrations below the tropopause – the goal is to decrease these with the DynOzone + MACC Reanalysis strategy

## Slide 57: Stratospheric intrusion analysis/DynOzone + Ozonesonde
On the surface level, the DynOzone + Ozonesonde method distinguishes itself from the other three methods by expressing the most ozone
The overrepresentation of ozone is not only present in the stratospheric intrusion, but also across the entirety of the surface
Looking at the vertical cross section, this overestimation is present yet again. The red contour level are almost all beyond the tropopause and into the troposphere.
By design however, it does create a strong shape around the 2.0 PVU contour

## Slide 58: Stratospheric intrusion analysis/DynOzone + MACC Reanalysis
On the surface level, the DynOzone + MACC Reanalysis method is not representing the stratospheric intrusion as strongly
This is also represented in the vertical cross section, where the high contour values do not as strong a shape around the stratospheric intrusion as a result of this low expression of ozone in the area of the intrusion
However, the area below the tropopause is represented with lower concentrations than the MACC Reanalysis, which was intended
In this case, the DynOzone + MACC Reanalysis performed no better than the MOZART4 seasonal average CLBC’s
It is, however, overall much lower than the DynOzone + Ozonesonde, which was intended

## Slide 59: Comparison of the four CLBC models over the western lateral boundary for GEM-MACH at April 13, 2010 21:00:00 GMT. The black contour is the thermal tropopause, the white contour is a dynamic tropopause based off a potential vorticity contour of 2.0 PVU. The teal contours are the kinetic energy from GEM-MACH indicating location of any jet streams through the lateral boundaries.

## Slide 60: Western LBC/MOZART4
The current operational method for the regional GEM-MACH model with chemical lateral boundary conditions isn’t ideal for definition of the ozone field at the tropopause
Using seasonal averaged chemical lateral boundary conditions based on MOZART4 provides an inaccurate model, the ozone gradient doesn’t follow the tropopause
Tropospheric ozone modelled off seasonally averaged MOZART4 based western lateral boundary conditions on April 13th, 2010. The black contour is the thermal tropopause, the white contour is a dynamic tropopause based off a potential vorticity contour of 2.0 PVU. The teal contours are the kinetic energy from GEM-MACH indicating location of any jet streams through the lateral boundaries.

## Slide 61: Western LBC/Ozonesonde based DynOzone
Previously, it was found that using chemical lateral boundary conditions based on ozonesonde climatologies and the DynOzone method provides a stronger shape around the tropopause contours
Noticeably, the 2.0 PVU contour is considerably closer to the quick shift between tropospheric and stratospheric ozone
Tropospheric ozone modelled off Ozonesonde based western lateral boundary conditions and the DynOzone method on April 13th, 2010. The black contour is the thermal tropopause, the white contour is a dynamic tropopause based off a potential vorticity contour of 2.0 PVU. The teal contours are the kinetic energy from GEM-MACH indicating location of any jet streams through the lateral boundaries.

## Slide 62: Western LBC/MACC Reanalysis
Using chemical lateral boundary conditions based on the ECMWF’s MACC Reanalysis also provides a strong shape around contours, however, the tropospheric ozone is found to be too high.
Similar to the DynOzone + ozonesonde CLBC model, the 2.0 PVU contour is considerably closer to the quick shift between tropospheric and stratospheric ozone
The discrepancy between the thermal and 2.0 PVU contours and the ozone shape is due to different meteorological conditions used for modelling
Tropospheric ozone modelled off seasonally averaged MACC Reanalysis based western lateral boundary conditions on April 13th, 2010. The black contour is the thermal tropopause, the white contour is a dynamic tropopause based off a potential vorticity contour of 2.0 PVU. The teal contours are the kinetic energy from GEM-MACH indicating location of any jet streams through the lateral boundaries.

## Slide 63: Western LBC/MACC Reanalysis DynOzone
Using the MACC Reanalysis dataset with the DynOzone method, there does not exist enough ozone in the stratospheric portions of the tropopause
The benefit is low ozone below tropopause
Tropospheric ozone modelled off MACC Reanalysis + DynOzone method based western lateral boundary conditions on April 13th, 2010. The black contour is the thermal tropopause, the white contour is a dynamic tropopause based off a potential vorticity contour of 2.0 PVU. The teal contours are the kinetic energy from GEM-MACH indicating location of any jet streams through the lateral boundaries.

## Slide 64: Next Steps
For the period of April to June 2010, the CLBC’s will be tested for the regional GEM-MACH on Hare and Brooks
Currently, a benchmark is being ran using MOZART4 seasonal climatologies on Brooks
  It should be complete by the time this is presented
  Another run using the DynOzone method + MACC Reanalysis dataset is being conducted on the new system
The MACC Reanalysis and DynOzone method CLBC’s will also be ran with MACC Reanalysis updated every 6 hours and DynOzone method CLBC’s ran on the same period for further comparison
Further surface analysis will be run on the new system to compare with station data

## Slide 65: Final notes
A (more technically detailed) report will follow this presentation in the coming days (August 28-31)

## Slide 66: The End!